## Slide 2
Congestion Setup & Initiation Enhancement
Problem Statement |  | Goal Statement
In order to create Congestion setup it requires 4 Linux systems. Setting up on all this systems takes time. Initiating UDP throughput traffic on all the devices one by one consumes more time. |  | Setting up Congestion in a single Linux system by adding networks statically of different IP subsets using a USB to Ethernet Dongle adapter. Script to automate the UDP throughput run on all devices automatically.
Start Date: 18-09-2019 End Date: 01-10-2019 Primary Metric: AHT |  | Project Lead: Karthikeyan Nanjundan ACES Consultant:

## Slide 3
How are we going to follow this Process?
Setting up congestion on a single Linux system with the use of Static Network addition with different subsets by a USB to Ethernet adaptor. In order to run the UDP traffic of each device a script can be used to automatically initiate UDP on all devices.
2. Who will be using?
FOSDA Conn TA and Connectivity QA teams will be using it of testing purpose. The setup will also be useful of other teams who seek congestion environment for their test requirement.
SOP

## Slide 4
Kaizen Charter
Business Case |  | Benefit
Congestion setup usually requires 4 Linux systems to run. Each system connected to different Wi-Fi routers. Manually running UDP throughput traffic on each device consumes lots of time and sometimes confuses. |  | New setup needs only 1 Linux system and the congestion setup can be done more easily and faster. Saves Cost of systems and saves time for setup. The script to automate UDP throughput run on all devices. This script instantly starts the Traffic and the congestion environment attains soon. It saves lots of time than manual.

## Slide 5: Setup Requirements
Previous Congestion Setup:
In previous setup, 3 Ubuntu PC required to setup congestion.
Operate on 3 systems separately to configure 3-APs and 3-Devices.
Cost of setup - $1684.26
New Congestion Setup:
Requires 1 Ubuntu PC connected to 3-APs and 3-Devices.
Operate with APs and Devices simultaneously.
Cost of setup – $561.42
Total Cost Save:
Total of $1122.84 saved with the new Congestion Setup.

## Slide 6
Manual Method of Initiating Congestion Environment:
Average time taken to Setup Congestion Systems: 61 Minute 14 Seconds.
Average time taken to Initiate Congestion Environment Manually : 30 Minutes 09 Seconds.
Average total time taken for whole process: 91 Minutes 23 Seconds.
Script Method to Initiate Congestion Environment:
Average time taken to Setup Congestion Systems : 15Minutes 12 Seconds.
Average time taken to Initiate Congestion Environment with script : 30 Seconds.
Average total time taken for whole process: 15 Minutes 42 Seconds.
Time Saved for a Setup:
Average time save: 75 Minutes 41 Seconds
Wiki: New Congestion Setup and Automation Script (Time & Motion Study)
Time & Motion Study

## Slide 7
Benefit Quantification
The below data's shows the difference between before and after implementing of this Method.

## Slide 8
Project contributors
Task | Responsibility
Owner | nkrt@